## Slide 1
Wireless Ad-hoc Network
Submitted to:
Abdullahil Kafi
Associate Professor, Dept of CSE
IIUC
GROUP- 5
Muhammad Muntasir Arefin Chowdhury(C153047)
Muhammad Mahi-Al-Jawad(C153010)
Md. Mofasser Hossain(C153031)

## Slide 2
What is Wireless Ad-hoc Network?
An ad-hoc network is a network that is composed of individual devices communicating with each other directly.
A wireless ad-hoc network (WANET) or MANET (Mobile ad hoc network) is a decentralised type of wireless network. The network is ad hoc because it does not rely on a pre-existing infrastructure, such as routers in wired networks or access points in managed (infrastructure) wireless networks.

## Slide 3
Types of WANETs
There are two types of Wireless Ad-hoc Networks.
        Fixed Ad-hoc Networks.
        Mobile Ad-hoc Networks(MANET).

## Slide 4
Fixed Ad-hoc Wireless Networks
The nodes are stationary
The connections among the nodes are static
Example: Wireless Sensor Networks (WSNs):
Senor nodes collect certain information:
Temperature, humidity, voice, image, etc.
Route data packets to a central base station.
The network topology is fixed; unless a node:
Shuts down
Runs out of energy

## Slide 5
Mobile of Ad Hoc Networks
The nodes are mobile.
The network topology is dynamic:
Node connectivity may vary with time due to:
  The dynamic nature of the wireless medium
  Node mobility, departure, new arrival, power outage, etc.
Hence, routing information changes accordingly.
Thus, efficient routing protocols are essential.

## Slide 6
Characteristics
Do not rely on fixed infrastructure
  No centralized administration
  No single point of failure
Nodes are connected directly
Each node functions as both a host and a router
  Hence, multi-hop routing is needed sometimes
Each node should be able to:
  Detect the presence of other nodes
  Identify the corresponding services and attributes
  Handle topology changes and malfunctions in nodes

## Slide 7
Why Ad-hoc Networks​?
No infrastructure needed
Can be deployed quickly, when no wireless communication infrastructure present
Can act as an extension to existing networks
Adaptive computing and self-configuring
Cost-effective

## Slide 8
Applications
Public safety and emergency operations:
  Search-and-rescue
  Police and fire-fighter networks
Military environments:
  Soldiers, tanks, planes, etc.
Civilian environments:
  Taxi cab network
  Meeting and conference rooms
  Sports stadiums
Personal area networking:
  Smartphone, PAD, laptop, headset, wrist watch, printer, etc.

## Slide 9
Search and Rescue Operations
Medical and rescue service during disasters:
  Fast and effective communication
  Real-time voice communication
  Secure and reliable medical record exchange

## Slide 10
Military Battlefield
Quick and dynamic network setup:
  No infrastructure
  Highly-mobile (fast topology changes)
Distributed, diverse, and reliable network:
  Fast adaptation to mobility and scale
  No single point of failure
  Secure and efficient communication
  Support for multicast routing

## Slide 11
Our Network

## Slide 12
Jazakallahu Khair….